## Slide 1
Robotics
2. Industrial robotics design principles

## Slide 2: 2. Industrial robotics design principles
2

## Slide 3: Learning outcomes
You will be able to:
List some common types of industrial robot design, identify key features and work envelopes of each type.
Describe the operation of a closed-loop servo control system for a robot joint.
3
2. Industrial robotics design principles
Identify applications of each robot type, using your examples to contrast robotics with automation.
Image © This Is Engineering

## Slide 4: Industrial robot designs
4
Different robot designs provide optimal solutions to a wide range of material handling and processing tasks.
The key difference is in how each design uses rotary or linear actuators to create different axes and types of movement.
Articulated arm
Cartesian/
Gantry
Polar/
Cylindrical
Spherical
SCARA
Delta
How would you describe each of these industrial robot designs?
What design features make each one distinctive?
2. Industrial robotics design principles

## Slide 5: Industrial robot designs
5
Articulated arm
Base with rotating joint
Two to ten further joints each provide a degree of motion
Cartesian/Gantry
One, two or three dimensions (axes)
High accuracy
Desktop to extremely large
SCARA
Selective Compliance Assembly Robot Arm
Rotary joints enable x-y motion
Faster than cartesian
Spherical
Two rotary joints control direction
One linear joint controls extension
Polar/Cylindrical
Rotating shaft and extendible arm
Cylindrical robots can also move up and down the shaft
Delta
Three arms control the working end of the robot
Light payloads only
Very fast and precise
2. Industrial robotics design principles
Identify one advantage and one limitation of each design.
Suggest some industrial sectors and working environments where each design might be used.

## Slide 6: Answers
Articulated arm
Cartesian/
Gantry
Polar/
Cylindrical
Spherical
SCARA
Delta
+
-
Scalability
Large floor area required
Relatively simple
Can’t reach around objects
Large work space
Restricted reach within workspace
Almost complete freedom of movement
Complex to program
Fast
Limited to two dimensions
Fast and accurate
Light payloads only
6
2. Industrial robotics design principles

## Slide 7: Answers
7
Assembly
Welding
Coating
Picking
Packing
CNC
Milling
Material handling
Assembly
Palletising
Assembly
Coating
Machine tending
Material handling
Pick and place
Die casting
Injection moulding
Welding
Material handling
What information might an engineer want to know when selecting and placing robots in a work cell?
2. Industrial robotics design principles
Articulated arm
Cartesian/
Gantry
Polar/
Cylindrical
Spherical
SCARA
Delta

## Slide 8: Work envelopes
8
Engineers need to understand the volume and shape of the space each type of robot (and specific models) can reach, and any limitations on this. The work envelope is the volume of space that the end of the robot arm can reach. Each type of robot has a distinctive work envelope.
Sketch the work envelope for each type of robot.
Give reasons why a robot arm may not be able to complete all tasks in all parts of its work envelope.
Suggest why the effective work envelope for a robot with a tool may differ slightly.
Articulated arm
Cartesian/
Gantry
Polar/
Cylindrical
Spherical
SCARA
Delta
2. Industrial robotics design principles

## Slide 9: Answers
9
Sketch how a control system can enable precise control.
A robot may not be able to carry its maximum payload at full extension.
A tool may extend the work envelope (including dead space) by the length of the tool.
A robot needs to accurately and precisely sense its position in its working envelope.
Articulated arm
Cartesian/
Gantry
Polar/
Cylindrical
Spherical
SCARA
Delta
2. Industrial robotics design principles

## Slide 10
Closed loop servo control systems
Servo stands for ‘servomechanism’ and describes any system that includes negative or ‘balancing’ feedback that reduces any error.
A motor is given instructions to rotate a robot arm joint.
A rotary encoder reports the rotary position of the joint 500 times per second.
Motion instructions
Motor
Input
Motor controller
Rotary encoder
Error
Feedback
10
2. Industrial robotics design principles
Discuss how the diagram illustrates negative feedback.
Output
Joint motion

## Slide 11: Robotics v automation: what do you think?
Robotics and automation are closely related and both make use of microprocessors, PLCs and control loops.
2. Industrial robotics design principles
11
Are automation and robotics the same thing?
Is robotics a subset of automation, or can you think of other examples of robotics that go beyond this? Which Venn diagram best represents your view?
Automation
Robotics
Robotics
Automation