## Slide 1
Microcontroller systems 2. Sensors and signals

## Slide 2: 2. Sensors and signals
2

## Slide 3: Learning outcomes
Perform calculations to find output voltage and digital outputs.
Understand the role of signal conditioning and analogue to digital conversion.
You will be able to:
Select a sensor component to match a functional specification.
3
Image © Ocado Technology

## Slide 4: Control systems recap
What is the role of each part of this control system?
What do the arrows represent?
What is the importance of feedback in a control system?
How many examples of input devices or sensors can you name?
Electronic controller
Output device
Sensor
Input
Output
Feedback
Input device
4

## Slide 5: Sensors and output signals
On the activity sheet, list some sensors that produce each type of output.
Discuss how you would describe how each output signal changes and what values the signal can have.
On
Off
Max
Min
255
0
5
Input devices and sensors can create a variety of output signals.
Linear encoder
Variable resistor
Push switch

## Slide 6: Sensors and output signals - answers
On
Off
Max
Min
255
0
6
Microswitch
Tilt switch
Reed switch
Magnetic switch
Push button switch
Thermistor
Variable resistor
Light-dependent resistor
Flow meter
Rotary encoder
Linear encoder
Accelerometer
Digital temperature
sensor
Sensors
Sensors
Sensors
Push switch
Variable resistor
Linear encoder

## Slide 7: Analogue signal conditioning
Signal conditioning converts analogue output signals to a common range.
This allows microcontrollers and PLCs to use a standard input circuit.
One common standard is for sensors to produce a current from 4 mA (min) to 20 mA (max).
This can be converted into 1 - 5 V by passing the current through a 250 Ω resistor.
Complete the table on your activity sheet to show:
What output these three sensors will produce across a 250 Ω resistor.
What reading each output current represents.
What digital resolution is possible with 256 steps.
What digital output the ADC would give for each reading.
Identify why a minimum current of 4 mA may be helpful.
Unit | Range | Output current
oC | 0 to 100 oC | 12 mA
mm | 0 to 200 mm | 16 mA
Bar | 0 to 1 Bar | 6 mA
E.g. a sensor produces an 8 mA current. 0.008 x 250 = 2 V.
7

## Slide 8: Analogue to digital converters (ADCs)
After signal conditioning, a sensor’s analogue output voltage may be converted into a digital signal.
The resolution (number of possible digital values) depends on the number of ‘bits’ the ADC uses.
What resolution is possible for the sensors in the table below?
What digital output would the ADC give for each reading?
Discuss why the resolution may not be the same as the sensor’s sensitivity.
Unit | Range | Output voltage
oC | 0 to 100 oC | 3 V
mm | 0 to 200 mm | 4 V
Bar | 0 to 1 Bar | 1.5 V
8
An 8-bit ADC represents 4 to 20 mA or 1 to 5 V as digital values from 0 to 255.
This ADCs digital output for a sensor output aV is
256 x (a-1) 4

## Slide 9: Answers
Analogue signal conditioning
4 mA helps to identify faults, which may produce zero current.
4 mA can also provide power for active sensors.
Unit | Range | Output current | Output voltage | Reading
oC | 0 to 100 oC | 12 mA | 3 V | 50C
mm | 0 to 200 mm | 16 mA | 4 V | 150 mm
Bar | 0 to 1 Bar | 6 mA | 1.5 V | 0.125 Bar
Unit | Range | Output current | Output voltage | Reading
oC | 0 to 100 oC | 12 mA | 3 V | 
mm | 0 to 200 mm | 16 mA | 4 V | 150 mm
Bar | 0 to 1 Bar | 6 mA | 1.5 V | 0.125 Bar
Analogue to digital conversion
The sensor may only be accurate to less than the ADCs resolution, for example, to the nearest 1C rather than 0.4 C.
Unit | Range | Output | Resolution | Digital output
oC | 0 to 100 oC | 3 V | 0.4 oC | 128
mm | 0 to 200 mm | 4 V | 0.8 mm | 192
Bar | 0 to 1 Bar | 1.5 V | 0.004 Bar | 32
9

## Slide 10: Sensor specifications table
Component | Specification | Output signal
Rotary encoder 1 | 0 to 360o, free rotation, 24 steps per revolution, absolute | Digital, 8-bit
Tachogenerator 1 | 9 mV/RPM, 10 mm shaft, +/-3% | 0 to 250 V, analogue
Thermistor 1 | 0 to 100 oC, 0.5o resolution, steep slope | 1 to 5 V, analogue
IR sensor 1 | 2 uM, 0 to 1000 oC, 1o resolution | 4 to 20 mA via USB or analogue
Rotary encoder 2 | 0 to 360o, free rotation, 360 steps per revolution, incremental | Digital, 12 bit
Thermistor 2 | 0 to 250 oC, 0.5o resolution, weak slope | 1 to 5 V, analogue
Tachogenerator 2 | 10 mV/RPM, 10 mm shaft, +/-5% | 0 to 250 V, analogue
IR sensor 2 | 5 uM, 0 to 500 oC, 0.1o resolution | 4 to 20 mA via USB
Thermistor 3 | 0 to 100 oC, 0.1o resolution, steep slope | 1 to 5 V, analogue
IR sensor 3 | 5 uM, 0 to 1000 oC, 0.5o resolution | 4 to 20 mA, analogue
Rotary encoder 3 | 0 to 360o, free rotation, 360 steps per revolution, absolute | Digital, 12 bit
Tachogenerator 3 | 10 mV/RPM, 10 mm hollow shaft, +/-5% | 0 to 250 V, analogue
10

## Slide 11: Select the right sensor
Role: Design engineer
Sector: Renewable energy
Application: Measuring the angular position of a wind vane on a turbine
Specification: 360 rotation, digital output, 1 resolution, absolute position
Role: CNC maintenance engineer
Sector: Manufacturing
Application: Measuring rotational speed of CNC router spindle
Specification:
10 V/ 1000 RPM,
10 mm hollow shaft, +/- 5% accuracy
Role: HVAC engineer
Sector: Commercial greenhouses
Application: Measuring air temperature so tomatoes can be kept at 21 to 24C
Specification: 0 to 50 C, 0.1 C resolution, steep slope (fast resistance change with temperature)
Role: Process improvement engineer
Sector: Food production
Application: Detecting whether jars of baby food have reached sterilisation temperature
Specification: Non-contact, 5 µM wavelength, 70 to 120 C, 0.1 C resolution
11

## Slide 12: Select the right sensor
Process improvement engineer
Design engineer
CNC maintenance engineer
HVAC engineer
Sensor: IR sensor 2
Reason: 5 uM, 0 to 500C, 0.1 resolution
Needs an IR sensor
Correct wavelength passes through glass
Correct range
Correct resolution
Sensor: Rotary encoder 3
Reason:
0 to 360, free rotation, 360 steps per revolution, absolute
Free rotation
Absolute position
Sufficient resolution
Sensor: Tachogenerator 2
Reason: 10 mV/RPM, 10 mm shaft, +/-5%
Correct shaft diameter
Sufficient accuracy
Correct output
Sensor:
Thermistor 3
Reason:
0 to 100C, 0.1 resolution, steep slope
Needs a thermistor
Correct range
Correct resolution
Correct slope (a steep slope provides a greater range of output values)
12

## Slide 13: Classifying sensors
Passive sensor
(responds
to its environment, so does not require a power source)
Active sensor (requires a power source to emit a signal that is scattered back to the sensor)
Reed switch
3-axis accelerometer chip
Laser distance
Analogue output
Digital output
Light-dependent resistor (LDR)
13