## Slide 1
Battery technologies 2. Cell chemistry

## Slide 2: 2. Cell chemistry
2

## Slide 3: Learning outcomes
You will be able to:
Describe the parts of a basic electrical cell.
3
2. Cell chemistry
Describe how a simple electrical cell produces electricity.
Explain the difference between primary and secondary cells.
Identify how primary and secondary cell discharge characteristics vary, linking this to applications.
Analyse the energy density of different cell types and use this to explain their relative advantages.

## Slide 4: What happens in a cell?
A cell converts stored chemical energy into electrical energy.
Any simple cell includes a cathode, anode and electrolyte.
The cathode and anode are made of different metals, for example manganese and zinc.
The use of different metals creates a potential difference (voltage) across the cell.
The electrolyte is a solution or paste that can conduct electricity.
4
4
What happens when a cell is connected in a complete circuit, for example, to an LED?
Given your answer, what do you think must happen inside the cell?
Can what happens inside the cell continue indefinitely, and what evidence supports your answer?
2. Cell chemistry
Anode
Cathode
Electrolyte

## Slide 5: What happens in a cell?
When the cell is connected in a complete circuit a current flows through the wire and the LED lights up.
This means that the current must also flow within the cell. The electrolyte enables this to happen.
A reaction takes place within the cell between the anode and cathode, which releases the cell’s stored chemical energy. This reaction can’t continue indefinitely. The cell only works until the stored chemical energy is used up and the reaction stops.
5
5
2. Cell chemistry

## Slide 6: Examples of cells
6
6
Which of these cell types are familiar to you?
Can you use your real-life experiences to divide them into two types of cell?
What difference explains your choices?
2. Cell chemistry
Zinc
Alkaline
Nickel metal hydride (NiMH)
Lithium ion (Li)
Nickel cadmium (NiCad)
Long life
NiMH
NiCad
Li

## Slide 7: Primary v secondary cells
7
The difference is whether the cells are used once or can be recharged.
In any cell a voltage and electric current will be produced until the reaction can no longer continue. The cell is discharged.
When a zinc or alkaline cell is discharged it can’t be recharged: this is a primary cell. A NiCad, NiMH or lithium ion cell can be recharged: this is a secondary cell.
Zinc or alkaline cells use one-way chemical reactions to produce electricity. What kind of reaction do you think happens inside secondary cells?
What does it therefore mean to recharge a cell?
What energy source provides this ability to recharge?
2. Cell chemistry

## Slide 8: Characteristics of primary v secondary cells
8
An engineer wants to know whether to use a lithium or alkaline cell to power a handheld measurement device. They carry out an investigation to find out how each type of cell discharges over time. They connect each type of cell to an identical load and measure the voltage across the load every 10 minutes.
The table shows how each cell’s voltage declines over time. Note that this is as a percentage of the maximum value. The engineer knows that rechargeable cells can have a lower terminal voltage, for example rechargeable AA cells are 1.2 V instead of 1.5 V, which can limit certain uses.
Plot a line graph to compare how each cell discharges over time.
Describe the difference and suggest how an engineer might use this information when selecting cells to power a device.
Would you use lithium or alkaline cells to power a TV remote or cordless drill? Justify your answers.
2. Cell chemistry
Load voltage as % of maximum
Time mins | Lithium % | Alkaline %
10 | 98 | 95
20 | 96 | 82
30 | 92 | 70
40 | 89 | 58
50 | 86 | 45
60 | 82 | 33
70 | 74 | 18
80 | 0 | 0

## Slide 9: Characteristics of primary v secondary cells
9
The graph shows that lithium cells retain a much higher working voltage as they discharge, while alkaline cells lose voltage steadily.
Lithium cells are suitable for devices where it is important to always provide as close to the working voltage as possible, for example when powering a DC motor.
Alkaline cells are suitable for non-critical applications like a TV remote.
Lithium cells are more suitable for critical or motor applications like cordless drills, drones, electric vehicles (EVs) or autonomous guided vehicles.
EV batteries need to output a consistent voltage to maintain speed, but what cell factor will affect the range of the vehicle?
How does this link to the overall design of the vehicle?
2. Cell chemistry
Time (mins)
0 20 40 60 80
Lithium
Alkaline
% of maximum Voltage
100
75
50
25
0

## Slide 10: Energy densities of secondary cells
10
A key innovation in secondary cells has been to increase their energy density, measured as the energy available per unit of mass or volume.
This matters for EVs as better energy density delivers more range, and more energy-dense battery packs take up less volume within the car.
2. Cell chemistry
Describe how the energy density of lead acid, nickel metal hydride and lithium polymer cells differs.
Why do you think nickel metal hydride cells have replaced nickel cadmium cells?
In total, roughly how much more energy-dense is a lithium polymer cell per litre, compared with a lead-acid cell?
50
100
150
200
250
300
350
400
450
50
100
150
200
250
Lithium polymer
Lithium phosphate
Nickel metal hydride
Nickel cadmium
Lead acid
Watt-hours/litre
Watt-hours/kilogram
Lithium ion
0
0

## Slide 11: Case study: freeze-thaw cell chemistry
11
A new freeze-thaw cell technology may make long-term, seasonal energy storage possible.
The cell’s electrolyte is a type of salt that is liquid at 180 °C but solid at room temperature. The cell is heated before being charged. When the cell cools the electrolyte solidifies, effectively ‘locking up’ the energy until needed. When needed, the cell is heated to allow a current to flow.
The technology is at an early stage of development but in laboratory tests a freeze-thaw cell has retained 92% of its capacity for three months.
What do you think happens to the electrolyte ions during the freeze-thaw process?
How might this type of cell make renewable energy more available over seasonal periods of time?
2. Cell chemistry

## Slide 12: Case study: flow batteries
12
Flow batteries store energy in tanks of liquid electrolytes made of iron salts.
To store energy inside the cell, one electrolyte is pumped past a positive electrode, depositing iron, and the other past a negative electrode, gaining electrons. This can store large amounts of chemical energy over long periods.
To produce electricity, the direction of the pumps is reversed so the electrolytes flow in the reverse direction past the electrodes, producing a current.
These cells have low energy density but use much safer chemistry than lithium-ion cells. Because the energy is stored in the electrolyte, to increase a flow battery’s storage capacity, engineers just increase the size of the electrolyte storage.
What applications might benefit from this form of energy storage?
Can you suggest how this concept might one day be adapted for electric vehicles?
2. Cell chemistry
Catholyte tank
Ion-selective membrane
Pump
Anolyte tank

## Slide 13: New cell technologies and engineering
Henry EV technician
I convert classic cars from petrol to EV systems.
How might each engineer’s role be changed as new cell technologies come to market?
Samira Power engineer
I design the systems that respond to short-term peaks in demand.
Vicky Recycling engineer
I develop new ways to recycle precious materials, including the rare earth metals used in modern secondary cells.
2. Cell chemistry
Jamal Home renewables
I install home solar power generation and storage.
Katrina Maintenance engineer
I maintain the automated warehouse vehicles in a busy warehouse.
13

## Slide 14: Learning outcomes
You will be able to:
Describe the parts of a basic electrical cell.
14
2. Cell chemistry
Describe how a simple electrical cell produces electricity.
Explain the difference between primary and secondary cells.
Identify how primary and secondary cell discharge characteristics vary, linking this to applications.
Analyse the energy density of different cell types and use this to explain their relative advantages.