## Slide 1
Electrical machines
2. Investigating torque, speed and current

## Slide 2
2
Electrical machines
2. Investigating torque, speed and current

## Slide 3: Learning outcomes
You will be able to:
Calculate the mechanical power of a motor based on its rotational speed and torque.
Image © This Is Engineering
3
2. Investigating torque, speed and current
State the formula for calculating the output power of an electric motor.
Describe how torque and speed vary with current in a series-wound and shunt-wound DC motor.

## Slide 4: Torque, speed and current in DC motors
Torque and speed vary with current in different ways in series, shunt and compound DC motors:
In a series-wound motor:
Torque is proportional to the square of the current. Speed is inversely proportional to the square of current.
In a shunt-wound motor:
Torque is proportional to current. Speed is inversely proportional to current.
In the sketch graphs, identify which of motors A and B is series-wound and which is shunt-wound.
Motor C is compound-wound. Its torque and speed characteristics are a compromise between series and shunt. Describe how motor C’s characteristics might look on each graph.
4
2. Investigating torque, speed and current
Current (A)
Torque (Nm)
Current (A)
Speed (RPM)
A
B
A
B

## Slide 5: Torque, speed and current in DC motors
5
2. Investigating torque, speed and current
A compound-wound motor’s torque and speed characteristics are midway between those of series and shunt-wound motors.
These speed and torque characteristics can be combined to identify how speed varies with torque:
The current draw through a motor is dependent on the load.
Use the speed v current graph to explain why it might be dangerous to start a series-wound motor with no load.
Use this graph to explain why a series-wound motor is a better choice for when a heavy load must be moved from rest.
Current (A)
Torque (Nm)
Current (A)
Speed (RPM)
Torque (Nm)
Speed (RPM)
A Shunt
B Series
C Compound
A Shunt
B Series
C Compound
A Shunt
B Series
C Compound

## Slide 6: Investigating torque and current
The Electrical machines interactive tool supports a range of investigations into the relationships between load, torque, speed, power and efficiency.
1. Use the sliders to set the radius and mass
2. Click on the switch to run the motor every time you set the radius and mass.
3. Observe how the values change.
Set r = 0.1 m and, for the range of values for mass, plot a chart of torque (y axis) against current draw (x axis).
Use your chart to identify whether this is a series or shunt-wound motor.
2. Investigating torque, speed and current
6

## Slide 7: Investigating torque and current – answer
7
The motor demonstrates a linear relationship between torque and current.
This is a shunt-wound DC motor.
0.0
0.2
0.3
0.4
0.5
0.6
0.5
0.4
0.3
0.2
0.1
0.0
Torque (Nm) v Current (A)
Torque (Nm)
Current (A)
2. Investigating torque, speed and current

## Slide 8: Investigating lift speed
The motor is used to power a hoist. The operator wants to know how to lift different masses most efficiently. They can vary the radius of the pulley connected to the axle.
20 m
18 m
19 m
17 m
16 m
15 m
14 m
13 m
12 m
1
1 m
10 m
9 m
8 m
7 m
6 m
5 m
4 m
3 m
2 m
1 m
On/Off
Lift time: 00.00 s
Discuss whether this is an appropriate application for a shunt-wound DC motor.
Use the interactive tool to find what pulley radius hoists the mass at the fastest speed.
What do you predict about how lift speed will vary with radius?
Start with r = 0.1 m and m = 0.2 kg. Time the hoist. Change the radius and repeat your measurement to find r for the fastest lift speed at m = 0.2 kg.
2. Investigating torque, speed and current
8
12 V

## Slide 9: Investigating lift speed – answers
9
The motor must do work to raise the load. As the load gains height, it gains potential energy.
The faster the load rises, the faster the energy used in the motor is converted into this potential energy.
Torque (Nm) v Current (A)
Radius (m)
2. Investigating torque, speed and current
The lifting speed increases with radius to a maximum before decreasing.
What characteristic of the motor do you think is at its maximum when the lifting speed is at its maximum value?
0.1
0.2
0.3
0.4
0.5
2.0
1.5
1.0
0.5
0.0
Lift Speed (m/f)

## Slide 10: Angular velocity, torque and power output
When a force F moves, work is done where W = Fd
Power is the amount of work done per second: P = W so we can write that P = Fd
Since d is velocity v, we can say that P = Fv
The power is equal to the force multiplied by the velocity at which it is moving.
10
2. Investigating torque, speed and current
This force F moves a distance d at velocity v, in time t:
F
d
F
Can you suggest the equivalent of P = Fv for a force that rotates around a point?
t t
t

## Slide 11: Angular velocity, torque and power out
If a force F rotates it becomes a torque 𝞽.
We measure angular velocity ω in radians per second:
There are 2π radians in one complete revolution.
𝞽
P = 𝞽ω
𝞽
ω
For angular motion P = Fv becomes P = 𝞽ω
ω = speed N in RPM x 2π radians per second
60
(dividing by 60 converts ‘per minute’ to ‘per second’)
and so by substituting, we can write
P = 𝞽2πN
60
11
2. Investigating torque, speed and current
.
radius r
radius r
1 radian

## Slide 12: Understanding power, torque and current
This knowledge helps to explain why, in a shunt-wound DC motor, torque is proportional to current, as you previously found:
0.0
0.2
0.3
0.4
0.5
0.6
0.5
0.4
0.3
0.2
0.1
0.0
Torque (Nm) v Current (A)
Torque (Nm)
Current (A)
Remember that in a shunt-wound motor
V = E + IaRa
Since P = VI the mechanical power P = EIa
We also know that P = 𝞽ω
Hence 𝞽ω = EIa and so 𝞽 = Ia x E
ω
Torque is proportional to current.
12
2. Investigating torque, speed and current

## Slide 13: Investigating mechanical power
Radius (m) | Torque (Nm) | Rotation (RPM) | Power (W)
0.1 | 0.2 | 115.2 | 2.413
0.15 | 0.3 | 100.8 | 3.167
0.2 | 0.4 | 86.4 | 3.619
0.25 | 0.5 | 72 | 3.77
0.3 | 0.6 | 57.6 | 3.619
0.35 | 0.7 | 43.2 | 3.167
0.4 | 0.8 | 28.8 | 2.413
0.45 | 0.9 | 14.4 | 1.357
0.5 | 1 | 0 | 0
In the Electrical machines interactive tool, verify that Pout = 𝞽2πN
Choose two combinations of radius and mass. Use the values for torque, rotational speed and mechanical power to verify the relationship. Use π = 3.14159.
The table on the left shows how torque, rotation speed and power change as the radius increases when lifting a mass of 0.2 kg. (Remember that 1 W = 1 Nm/s). Use the power formula above to help you interpret the table and suggest why power increases to a maximum, but then decreases.
60
13
2. Investigating torque, speed and current

## Slide 14: Investigating mechanical power – answers
The mechanical power output is proportional to rotational speed x torque.
Rotational speed is inversely proportional to the radius:
… while torque is proportional to the radius:
… and when torque and rotational speed are multiplied within the power formula, this has the result of creating a curve for power output against radius:
For a fixed mass, increasing the radius increases the load on the motor. Hence the power of the motor first increases with load before decreasing after maximum power is reached.
How else could you verify this using the Electrical machines interactive tool?
What practical considerations do you think this power output curve raises for an engineer?
14
2. Investigating torque, speed and current
Radius (m)
Rotation (RPM)
Torque (Nm)
0.1
0.2
0.3
0.4
0.5
1.00
0.75
0.50
0.25
0.0
0.1
0.2
0.3
0.4
0.5
125
100
75
50
25
0.0
Radius (m)
Radius (m)
Power (W)
0.1
0.2
0.3
0.4
0.5
4
3
2
1
0.0
Fastest lift speed is at maximum power output

## Slide 15: Learning outcomes
You will be able to:
Calculate the mechanical power of a motor based on its rotational speed and torque.
Image © This Is Engineering
15
2. Investigating torque, speed and current
State the formula for calculating the output power of an electric motor.
Describe how torque and speed vary with current in a series-wound and shunt-wound DC motor.